## Slide 1: Understanding User Contention and Its Effects on Resource Allocation in Heterogeneous Networks
Dr Glenford Mapp
Associate Professor
Head of the C-ITS Research Group
Middlesex University, London

## Slide 2: Outline of this talk
Motivation for this research
Look at contention-based networks
Heterogeneous networking in highly mobile environments
Proactive resource allocation using contention analysis
Application to VANET networks
Questions

## Slide 3: Motivation
Users are demanding more of common networks by running applications that need Quality of Service support
New networks being deployed: 5G, 802.11p, tactile networks
Leading to heterogeneous networking
  Devices will have several network interfaces

## Slide 4: New Algorithms for new scenario
In the old world, a device was attached to only one network, so the concern was how the network would respond when a lot of users were using this one network
New heterogeneous networking environment : If one network is saturated, then devices can hand over to other networks
  Learning to manage several networks at the same time. Optimizing overall network perfrmance
  Need to understand how different networks are performing in response to user demand

## Slide 5: Deeper understanding of user contention
Contention is the competition for network resources based on user demand
It can be used to indicate how well a network can perform as user demand increases
Find the parameters for optimal performance
  Contention-based networks
    Pure ALOHA, Slotted ALOHA, etc.
  Server-based systems
    Queueing Theory

## Slide 6: Contention-based Networks
Users directly contend to use the network. So we either have a successful transmission or a collision
We need to find P success: the probability of a successful transmission
The throughput, Th = λP success
We need to understand how user demand affects the throughput, Th

## Slide 7: Analysis Parameters
There are N nodes in the network.
Each node acts completely independently of other nodes.
Packets to be transmitted are generated at average rate, λ
Packet arrival is a Poisson Process, i.e., the inter-arrival time is exponentially distributed
Each packet is transmitted in time T

## Slide 8: Pure ALOHA Protocol
A node transmits when a packet is generated.
If the node receives an ACK, then the packet was received OK
If no ACK, then a collision has occurred and the packet is retransmitted after a random back-off period
This analysis does not consider back-off

## Slide 9: Pure ALOHA
0
T
2T
t->
Successful transmission of a packet by a node at time T is given by:
P(node transmits at time T) &&
P (no other node transmits between 0 and 2T)
P(Success) = λe-λT e-λ2(N-1)T = λe-λ(2N-1)T P(Success) max = dP(Success)/dλ = 0
Solution: λ = 1/(2N-1)T P(Success) max for N nodes = N/(2N-1) T e -1
As N -> ∞, P(Success) max ~ ½ e-1

## Slide 10: Pure ALOHA
Throughput = Th = λP(Success) = λ2 e –λ(2N – 1)T
Th max = dT/dλ = 0
Solution λ = 2/(2N-1)T
For N nodes: Th max = 4N/((2N-1)T)2 e-2
As N-> ∞, Th max ~ (1/N) e-2

## Slide 11: Slotted ALOHA Protocol
All nodes on the network are synchronized using a global clock
Nodes can only transmit at predefined epochs usually at T, 2T, etc.
A node having a packet to send must wait until the next epoch at which time the packet is transmitted.
If no ACK, then a collision has occurred and the packet is retransmitted after a random back-off period

## Slide 12: Slotted ALOHA
0
T
2T
t->
Successful transmission of a packet by a node at time T is given by:
P(node has a packet to transmit between 0 and T) &&
P (no other node has a packet to transmit between 0 and T)
P(Success) = (1 – e-λT) e-λ(N-1)T P(Success) max = dP(Success)/dλ = 0
Solution: e-λT = (N-1)/N P(Success) max for N nodes = ((N-1)/N)N-1
As N -> ∞, P(Success) max ~ e-1

## Slide 13: Slotted ALOHA
Throughput = T = λP(Success) = λ (1 – e-λT) e –λ(N-1)T
Th max = dT/dλ = 0
Solution e-λT = [ 1 – (λT/NλT -1) ] Solution = λN for a given value of N
For N nodes: Th max = (NλN2T / (NλNT – 1) [ 1 – (λNT/NλNT -1) ] N-1
As N->∞, Th max ~ λNe-1
As N->∞, λ N ~ 0

## Slide 14: P success for Pure and Slotted ALOHA

## Slide 15: Benefits of this Approach
Examined the nature of contention in detail
Able to express such contention using probabilistic equations
Able to see the effect of loading the network
Can we apply this to other networks than just contention-based networks

## Slide 16: Mobile Networks

## Slide 17: Mobile Networks
We first define two circles represented by:
  Handover Radius: represents the communication between the base-station and the Mobile Node. Beyond this region, signals may not be detected.
  Exit Radius: For seamless handover, handover must begin at the Exit Radius so that handover is completed by the time the MN reaches the Handover Radius

## Slide 18: Mobile Networks – Classical Model

## Slide 19: Mobile Network Analysis
A Mobile Node (MN) can leave the system because:
  the MN uses the data channel and so is served
  The MN leaves the system due to mobility while being served
  The MN leaves the system due to mobility with no service
If we can detect the final case early; then we can signal to the MN that it is unlikely to get service in this network
In a heterogeneous environment, the MN can also be immediately signaled to go to another network.
  There is no waiting for a channel that the MN is not likely to ever get

## Slide 20: Building Future Networks (Y-Comm)

## Slide 21: Y-Comm
Seeks to provide mechanisms to build future networks
Solution: Integrate communications, mobility, QoS and security
Key Concepts:
  Time Before Vertical Handover (TBVH)
  Network Dwell Time (NDT)
Y-Comm also showed how TBVH and NDT can be calculated for any arbitrary network setup

## Slide 22: TBVH and NDT

## Slide 23: Requests for Resources
WIRELESS
NETWORK
REQ (Time , TBVH, NDT)
A
A
REQ (Time , TBVH, NDT)
B
B

## Slide 24: Contention Analysis
MNA needs channel at (Time + TBVH) A
MNA releases channel at (Time + TBVH + NDT)A
MNB needs channel at (Time + TBVH)B
MNB releases channel at (Time + TBVH + NDT)B

## Slide 25: There are 3 outcomes
No contention:
    (Time + TBVH)A < (Time + TBVH)B
    (Time + TBVH + NDT)A < (Time + TBVH)B
Contention: Two Types: Partial and Total
    (Time + TBVH)A < (Time + TBVH)B
    (Time + TBVH + NDT)A > (Time + TBVH)B
    Partial Contention:
    Total Contention:
(Time + TBVH + NDT)A < (Time + TBVH + NDT)B
(Time + TBVH + NDT)A >= (Time + TBVH + NDT)B

## Slide 26: Contention Analysis for 2 Nodes

## Slide 27: Request Summary
No Contention: Requests granted as requested:
  Channel granted at (Time + TVBH)A
  Channel released at (Time + TBVH + NDT)A
  Same with B
Partial Contention: Requests granted but modified for B
  Channel granted at (Time + TBVH + NDT)A
  Channel released at (Time + TBVH + NDT)B
Full Contention: Request for B not granted:
  Force B to handover to another network

## Slide 28: Analysis of Contention
P(Z=z) where Z is an exponential random variable of TA with mean: τA
P(Y=y) where Y is an exponential random variable of NA with mean: ηA
P(X=x) where X is an exponential random variable of TB with mean: τB
P(W=w) where W is an exponential random variable of NB with mean: ηB
No contention: z < x, g < x
Partial Contention: z < x, g > x, g < r
Full Contention: z < x, g > x, g > r

## Slide 29: Results
No contention = τA ηA
(τA + τB )(ηA + τB )
Partial Contention = τA τB ηA
(τA + τB )(ηA + τB ) (ηA + ηB)
Full Contention = τA τB ηB
(τA + τB )(ηA + τB ) (ηA + ηB)

## Slide 30: Results verified using an independent Discrete Event Simulation; Node A – (50,10)
No contention

## Slide 31
Partial Contention:
Full Contention:

## Slide 32: Further work
Also analyzed 3-node scenario:
General observations
  For N nodes:
  possible outcomes: is
    3 N-1 N
  General Formula for No contention

## Slide 33: First Model: Decision Model
Check for full contention as requests arrive. Nodes that would experience full contention are not allowed to join the channel queue:

## Slide 34: Second Model: Decision plus Contention queue
We introduce a queue called a contention queue into which requests for the channel are placed before the channel queue.

## Slide 35: Second Model
The effective rate into the channel queue is:
    λ ef f = λ (1 − α) * (1 – β)
New Queuing Model is:

## Slide 36: Results from Simulation and Analytical Models-MRT

## Slide 37: Results from Simulation and Analytical Model- Throughput

## Slide 38: Calculating α and β
α is calculated using the full contention model
β is calculated by comparing each entry in the queue with an incoming request.
  For the nth entry in the queue, the P( that the incoming request or the nth entry is ejected from the queue) is given by:
β is the sum of β(n) over all the entries in the queue:

## Slide 39: Graph of Results for β

## Slide 40: Application of results using the MDX VANET Testbed

## Slide 41: Calculating α for varying speeds

## Slide 42: Calculating β for varying speeds

## Slide 43: Future Work: Operational Space

## Slide 44: THANK YOU FOR LISTENING
QUESTIONS?