## Slide 1: A novel approach to verification of distributed system performance
Presentation for Mathematics of Networks Workshop, April 2019
Peter.Thompson@pnsol.com
Notes: Abstract: A key risk for time-critical distributed systems is that the performance will be unacceptable and/or uneconomic to deliver. Mitigating this risk requires an approach that supports both prospective validation and post-facto verification that should: capture performance requirements and resource constraints; validate them; construct performance properties/invariants that witness those requirements; and support the reification and abstraction of such properties/invariants throughout the System Development Life-Cycle. Here, we present a novel approach to prospective performance and resource consumption validation called the ∆Q framework, based on the use of improper random variables, which addresses these issues.

## Slide 2
Goals
Consider how to enable Validation & Verification of cost and performance
  for distributed and hierarchical systems
  using developments of well-tried tools
  supporting both initial and ongoing incremental development
Provide early visibility of cost/performance hazards
  avoiding costly failures
  maximising the chances of successful in-budget delivery of acceptable end-user outcomes
Partners
Supported by:
PEnDAR project
Notes: PEnDAR - Performance ENsurance by Design, Analysing Requirements TSB REFERENCE: 132304
Why? Seeing cost/performance hazards becoming visible late in the development process – too late to save some projects! Multi-$B problem worldwide
Pressure to re-purpose commodity infrastructure for safety/mission-critical objectives; need to be able to articulate a safety case.

## Slide 3: Focus on performance
Functional correctness is not enough

## Slide 4: Nature of performance
In an ‘ideal world’, systems would always respond instantaneously
  and without exceptions/failures/errors
In practice this doesn’t happen
  there is always some delay and some chance of failure: some attenuation
Thus performance is a privation
  the absence of attenuation
  like ‘darkness’ or ‘silence’
Quantity also matters
  require a certain rate or volume of responses with a given bound on attenuation

## Slide 5: Measure of performance: ∆Q
∆Q is a measure of the ‘quality attenuation’ of an outcome
  the extent of deviation from ‘instantaneous and infallible’
  nothing in the real world is perfect so ∆Q always exists
∆Q is conserved
  a delayed outcome can’t be ‘undelayed’
  a failed outcome can’t be ‘unfailed’
∆Q can be traded
  e.g. accept more delay in return for more certainty of completion
∆Q has an algebra
  can manipulate it mathematically
∆Q is composable
  supports hierarchical analysis

## Slide 6: Application performance depends only on ∆Q
Components of a distributed application (e.g. a client and a server) exchange information as streams of packets
  if those packets were all delivered instantaneously and the computational components performed correctly, the application would be guaranteed to work
  however, there is always quality attenuation, ∆Q
Whether the application delivers fit-for-purpose outcomes depends on the magnitude of the attenuation
  and the application's sensitivity to it
  the layering of network protocols isolates the application from any other aspect of the packet transport.
Notes: To the application the network is a necessary evil that delays and loses packets!

## Slide 7: Sources of attenuation
Synchronisation
  Implicit: resource sharing
  Exclusive
  Discrete:
  Locks etc
  Long timescales
  Statistical
  Continuous:
  CPU, interface…
  Short timescales
  Explicit
  Communication
  Data dependency
Causality
  Information:
  Takes time!
  Communicated
  Computed
Imperfection
  Discrete
  Statistical
  Exceptions
  Failures
  Resource exhaustion
Process algebra
Stochastic process algebra
∆Q Framework

## Slide 8: ∆Q in networks
Exchanging information via streams of packets sharing network resources gives tremendous flexibility, but introduces an element of chance
  because the state of the network when any given packet is inserted is unknowable, exactly what will happen to it is uncertain
∆Q in statistically-multiplexed networks is thus necessarily a probabilistic measure
  can be represented by an improper random variable
  encompassing normal behaviour and exceptions/failures in one model

## Slide 9: Representation of ∆Q
0.1
0.2
0.3
0.4
0.6
0.5
0.7
0.8
0.9
1.0
0.0
Cumulative probability
Response time
2
4
6
8
10
12
14
16
Tangible mass encodes distribution of response time
Intangible mass encodes probability of exception/failure
If we write ∆Q(x) for the probability that an outcome occurs in a time t < x, then the tangible mass T is defined by:
The intangible mass is simply 1 - T

## Slide 10: Outline of a coherent methodology

## Slide 11: Performance/resource analysis
Sub-system
Sub-system
Sub-system
∆Q
Shared resources
Starting with a functional decomposition:
Take each subsystem in isolation
  analyse performance
    modelling remainder of system as ∆Q
  quantify resource consumption
    may be dependent on the ∆Q
Examine resource sharing
  within system – quantify resource costs
  between systems – quantify opportunity cost
Successive refinements
  consider couplings
  iterate to fixed point
Quantitative Timeliness Agreement
Notes: A Quantitative Timeliness Agreement (QTA) is a relationship between the demand (the applied load, including its pattern) and the delivered quality attenuation (as a probability distribution, ∆Q)
Opportunity cost between one system and another sharing the same resources, and successive refinements won’t be considered in this webinar.

## Slide 12: Quantifying intent
The key challenge is to establish quantified intentions
  for outcomes/resources/costs
Then a variety of mathematical techniques can be applied
  queuing theory
  large deviation theory
  ∆Q algebra
This is “only rocket science”
  not brain surgery!
  set of tools already developed
Notes: Rocket science used to be something only world superpowers could do – now you only need to be a billionaire! It’s well enough understood to be reproducible, and is just (complex) engineering. Brain surgery requires experience, skill and gut feel – not easy to teach! Outcomes are hard to quantify.

## Slide 13: Quantifying timeliness
Outcome requirement:
Suppose we had a specification for how long it’s acceptable to wait for a system outcome:
50% of responses within 5 seconds
95% of responses within 10 seconds
99.9% of responses within 15s
0.1% failure rate
This can be represented by an improper CDF
0.1
0.2
0.3
0.4
0.6
0.5
0.7
0.8
0.9
1.0
0.0
Cumulative probability
2
4
6
8
10
12
14
16
Notes: A key challenge is to quantify timeliness rather than simply rates – this is key for any individual end user.
Let’s suppose we could agree how long it’s OK to wait for the first frame of a chosen video to start.
This is the “specification” as a CDF of the observable outcome – it represents the “worst case” observable behavior that would still fulfill the requirement
We are also defining that responses received after 15 seconds and loss are indistinguishable outcomes (from our point of view).

## Slide 14
Suppose the black line shows the delivered CDF
  from measurement, simulation or analysis
This is everywhere above and to the left of the requirement curve
  this means that the timeliness requirement is satisfied
  if not, there is a performance hazard
Meeting a timeliness requirement
0.1
0.2
0.3
0.4
0.6
0.5
0.7
0.8
0.9
1.0
0.0
Cumulative probability
Response time
2
4
6
8
10
12
14
16
)
Notes: Any CDF whose curve is always to the left and above this one represents an outcome that is “acceptable”. If the black line crosses the blue line we have a performance hazard.

## Slide 15: Validating performance requirements
Decompose the performance requirement following system structure
  using engineering judgment/best practice/cosmic constraints
  creates initial subsystem requirements
Validate the decomposition by re-combining via the behaviour
  formally and automatically checkable
  captures interactions and couplings
Necessary and sufficient:
  IF all subsystems function correctly and integrate properly
  AND all subsystems satisfy their performance requirements
  THEN the overall system will meet its performance requirement
Apply this hierarchically until
  behaviour is trivially provable OR
  have a complete set of testable subsystem verification/acceptance criteria
Notes: This can be combined with a corresponding analysis of the resource consumption

## Slide 16: Simple quantitative worked example

## Slide 17: Generic RPC
Front end
Back end
Network
6 Transmit Response
2
Send request
4
Process request
5
Commit results
1 Construct transaction
7
Receive Response
0
Idle
8
Complete transaction
3
Receive request
Notes: We consider a very generic remote procedure call in which a front end (which could be a web browser, an embedded sensor, a smart meter etc.) engages with a transaction across a network with a back end that includes an interaction with a database of some sort. This is illustrated in this slide, which shows the system components in blue and the typical sequence of events as numbered circles. RPC is a common design pattern:
DNS lookup
Web request
IoT sensor system
Billing system e.g. smart meters

## Slide 18: Generic RPC - observables
Front end
Back end
Network
6 Transmit Response
2
Send request
4
Process request
5
Commit results
1 Construct transaction
7
Receive Response
0
Idle
8
Complete transaction
3
Receive request
A
E
D
C
B
F
∆Q(A⇝B)
∆Q(B⇝C)
∆Q(C⇝D)
∆Q(D⇝E)
∆Q(E⇝F)
Notes: We measure the performance of the system on the basis of passage times between the labelled observation points A - F, which we characterise using improper random variables, ∆Q.

## Slide 19: Generic RPC – abstract performance
Front end
1 Construct transaction
0
Idle
8
Complete transaction
A
E
B
F
Network
6 Transmit Response
2
Send request
7
Receive Response
3
Receive request
D
C
∆Q(C⇝D)
Notes: From a quality attenuation perspective, we can ‘roll up’ the last stage of the process into a ∆Q – from the viewpoint of the rest of the system, how the transition from C to D occurs is irrelevant, we are just interested in how long it might take and how likely it is to fail (its ∆Q).

## Slide 20: Generic RPC – abstract performance
Front end
1 Construct transaction
0
Idle
8
Complete transaction
A
E
B
F
∆Q(B⇝E)
Notes: In the same way we can combine the network portions with the back end to give a composite ∆Q.

## Slide 21: Generic RPC – abstract performance
0
Idle
A
F
∆Q(A⇝F)
Notes: Finally we can roll up the front end behaviour to give the ∆Q for the whole system. This is the quality attenuation from the ‘user’ point of view, which is where we can start to impose requirements.

## Slide 22: Performance requirement
User performance requirement is a bound on ∆Q(A⇝F), e.g.
  50% within 500ms
  95% within 750ms
  etc.
Decompose this as ∆Q(A⇝F) = ∆Q(A⇝B) ⊕ ∆Q(B⇝E) ⊕ ∆Q(E⇝F)
How these terms combine depends on the behaviour
Notes: This is where we need to bring in a quantitative intent: how rapidly and reliably we want the system to perform. Here we choose some numbers for the sake of an example, which are plotted on the right as a CDF.

## Slide 23: Front-end behaviour (1)
Since the request or its acknowledgement may be lost, the process retries after a 333ms timeout
  failure mitigation
After three attempts the transaction is deemed to have failed
  failure propagation
Can unroll the loop for a clearer picture
A
E
B
F
Notes: We show the state diagram for the front-end process. Note that not every situation has an explicit notification of failure as we do here.
We’ll get round to C and D later!

## Slide 24: Front-end behaviour (2)
Notes: If N=4 we can unroll the process like this. We have a non-preemptive first-to-finish synchronisation between receiving the response and the timeout. Which route is taken is a probabilistic choice, shown here with blue and green examples. Which path is taken depends on the ∆Q of the B – E path, represented here by the ‘wait for response’ states.

## Slide 25: Performance analysis (1)
We have a non-preemptive first-to-finish synchronisation between receiving the response and the timeout
Which execution path is taken is a probabilistic choice depending on the ∆Q(B ⇝E)
  combine the ∆Qs of the different paths with these probabilities
Assumptions:
For an initial customer deployment over UK broadband with the server in the US East Coast:
∆Q(B⇝C) and ∆Q(D⇝E) the same:
  minimum delay 95ms
  50ms variability
  1-2% loss
∆Q(C⇝D) uniformly distributed between 25ms and 60ms
Notes: The network characteristics are assuming communication between a UK-broadband-connected front-end and a US East Coast cloud-located server.
Combining ∆Qs means convolving the corresponding probability distributions – this is mathematically quite straightforward and computationally inexpensive.

## Slide 26: Performance analysis (2)
∆Q(C⇝D)
∆Q(B⇝E)
∆Q(A⇝F)
Requirement
Notes: The first curve shows the server response ∆Q, the second its convolution (twice) with the network transport ∆Q.
On the right we see the result of combining this with the behaviour of the front-end, compared with the performance requirement.

## Slide 27: Verification
So far, the verification task seems straightforward:
  provided the network and server performance are within the given bounds, then the front end will deliver the required end-user experience
However, this seems to have plenty of slack
  can we validate a different set of requirements?
  how far can we relax them?
With this model we can explore:
  varying the network performance
    e.g. an alternate server on the US West Coast, with more routing choices
  varying the server performance (e.g. as a result of load)
    not today!
Notes: Having constructed a model, it is now easy to experiment with varying some parameters.

## Slide 28: Performance analysis (3)
∆Q(C⇝D)
∆Q(B⇝E)
∆Q(A⇝F)
Requirement
Notes: The server performance is the same but the network has higher delays – equivalent to having an alternate server on the US West Coast, with more variety of routing choices.
We can see on the right that the resulting overall ∆Q no longer meets the requirement.

## Slide 29: Summary
System performance validation consists of:
  analysing the interaction of system behaviour and subsystem performance requirements
  showing that this ‘adds up’ to meet the quantified requirements (QTA)
System performance verification consists of showing that subsystems meet their QTAs
  by analysis and/or measurement of ∆Q of the subsystems’ observable behaviour
This provides acceptance and/or contractual criteria for third-party subsystems or services
  substantially reduces performance integration risks and hence re-work

## Slide 30: Thank you!

## Slide 31: Backup slides

## Slide 32: Server resource consumption
Virtualised server has a limit on the rate of I/O operations
  So that the underlying infrastructure can be reasonably shared
  Such parameters affect the OPEX
Typically access is controlled via a token-bucket shaper
  Allows small bursts
  Limit long-term average use
  This constitutes a QTA
    Need to verify both sides
Delivered performance of the virtualised I/O thus depends on recent usage history
  Load is a function of number of front-ends accessing the service and the proportion of re-tries
  Re-tries depend on the ∆Q(B ⇝E) – which in turn depends on the performance of the I/O system!
This has been modeled here via a probability of taking a ‘slow path’ in the server

## Slide 33: Performance analysis (4)
∆Q(C⇝D)
∆Q(B⇝E)
Requirement
∆Q(A⇝F)
Notes: We now add in a probability of the server following a ‘slow path’ (which could be as a result of load exceeding an aspect of the virtualisation constraint), modeled as a uniform delay of between 15ms and 150ms. On the left we have five ∆Q curves for the server response, with the slow path probability varying from 0% (the original curve) to 25%, 50%, 75% and 100%.
On the right we see the ∆Q resulting from combining this with the front-end behaviour; even a 25% chance of following the slow path breaks the performance requirement.

## Slide 34: Capturing interactions
Notes: We’re now going to run through some of the technical dimensions of this challenge

## Slide 35
Outcomes Delivered
Resources Consumed
Individual impact
Variability
Exception/failure
System impact
Self-induced
Externally created
Individual impact
Mitigation
Correlation
System impact
Propagation
Scale
Schedulability
Capacity
Distance
Number
Time
Space
Density
Notes: This captures what we have learnt about system delivery problems over the last decade. There’s a lot here so we’re going to break it down!